## Slide 1: Honors Credit DDR in assembly
Spring 2024
Rupin Raj Kumar Pradeep

## Slide 2: Table of Contents
  Project Overview
  Specifications
  Block Diagram
  Functionality Diagram
  BOM
  Schematic
  Results/Outcomes
  Possible Improvements

## Slide 3: Project Overview Honors Experience Correlation
Create the popular old rhythm game Dance Dance Revolution in assembly
Include console animation using Putty
Play music during game play
Create a dance pad as input to the game
Creating Dance Dance Revolution in assembly is a culmination of the three classes I currently TA for under my teacher advisor: CSE 241 Digital Systems, CSE 341 Computer Organization, and CSE 379 Microprocessors
CSE 241: The hardware implementation of the dance pad used potentiometers for variable resistance increasing precision of the Analog-to-Digital Converter
CSE 341: Basic organization of assembly code
CSE 379: Experience creating a game in assembly and animating using the Putty serial console

## Slide 4: Specifications
Software:
Code Composer Studio - Uploading code to the Tiva C Series TM4C123GH6PM
Arduino - Input processing to play the selected song
Processing - Communication from Arduino to the PC for playing music
Putty - Display the console output of the game at specific settings
Constraints:
The beatmap file must be read at the very beginning of the program and must be small
Arduino and Processing are necessary to play music as Stellaris has no 64 bit drivers

## Slide 5: Block Diagram
TIVA C SERIES
Keyboard
Arduino
Processing
Putty
Computer Audio Ports
Dance Pad
UART
UART
ADC
Parallel Communication over wires
Serial Communication over COM port

## Slide 6: Functionality FlowChart
The game starts with a menu prompt
expecting Switch 1 on the TIVA as input
Then WASD is used to change song,
difficulty, start, or back
Once DDR starts, it mainly waits for
two interrupts, the timer for the game
loop and the user input
User input clears applicable arrows and
prints “good” or “perfect”
Timer is used to move the arrows up the
screen and generate “miss” when arrows
are missed
The song beatmap ends on a * in the file

## Slide 7: Bill of Materials
Just the game:
TIVA C Series TM4C123GH6PM
Arduino (preferably UNO)
4 male-to-male or 4 female-to-male wires
One Arduino to PC cable (Arduino USB to USB A)
One Tiva to PC Cable (Micro USB to USB A with data transfer capability)
Additional materials for the dance pad
EVA foam 5ft. x 2ft. thick Cut this and the one below into 1ft x 1ft squares
EVA foam 5ft. x 2ft. thin
4 potentiometers
4 pieces of velostat
Lots of male-to-male wires that will be long enough to connect the dance pad and the Tiva
5 male-to-female wires, 1 GND and the rest are for inputs to pins D0 to D3

## Slide 8: Schematic
U1
U0
L1
L0
D1
D0
R0
R1
Key: U = Up, D = Down, L = Left,
R = Right, 0 = VCC, 1 = user input
Copper tape on different layers (differentiated by color)
Computer
U0
D0
R0
L0
Pot
Pot
Pot
Pot
A
B
C
D
A
B
D
C
L1
U1
R1
D1

## Slide 9: Possible Improvements
  Using a C library for graphics and a GUI other than console
  Better use of velostat for making the dance pad sensors
  Using images instead of hardcoded values for each piece of art
  Finish more beatmaps
  Remove random printing glitches

## Slide 10: Links
Github Link: https://github.com/rupin-r/TivaCDownDownRight/tree/main
TIVA documentation: https://cse.buffalo.edu/~kds/cse-410/Docs/tm4c123gh6pm.pdf
Processing download: https://processing.org/download
Arduino download: https://www.arduino.cc/en/software
Code Composer Studio download: https://www.ti.com/tool/CCSTUDIO
Putty download: https://www.putty.org/